## Slide 1: “LOCK OUT/TAG OUT”
PPT-026-05
1
OSHA 29 CFR 1910.147
CONTROL OF HAZARDOUS ENERGY
LOCK OUT - TAG OUT
(LOTO)
Bureau of Workers’ Comp
PA Training for Health & Safety
(PATHS)
Notes: LOTO is on OSHA’s list of “Most-Cited” violations when the solution for companies can be remediated through implementation of a LOTO Program.

## Slide 2: Topics
PPT-026-05
2
Purpose of Standard
LOTO Program
Authorized & Affected Employees
LOTO Procedures & Program
Training, Inspections, Testing
Contractors
Notes: Topics discussed include:
Purpose of Standard
LOTO Program
Authorized & Affected Employees
LOTO Procedures & Program
Training, Inspections, Testing
Contractors

## Slide 3: LOTO Mishaps are Severe!
PPT-026-05
3
Average lost work days for failure to LOTO is 24 days per injury
120 workplace fatalities annually are related to failure to LOTO
Notes: The ramifications of an absent program can be severe.
Average lost work days for failure to LOTO is 24 days per injury
120 workplace fatalities annually are related to failure to LOTO

## Slide 4: Tag Center
PPT-026-05
4
Centralized point to keep appropriate tags
Notes: Your program should establish a Tag Center which is a centralized point at which to keep appropriate tags.

## Slide 5: Purpose of LO/TO Standard
PPT-026-05
5
If a risk exists to any person upon unexpected start up or sudden release of stored energy, all protective measures must be taken to isolate all sources of hazardous energy
Notes: The purpose of this standard as with all OSHA standards is to promote the safety of the employee in the workplace.
If a risk exists to any person upon unexpected start up or sudden release of stored energy, all protective measures must be taken to isolate all sources of hazardous energy.

## Slide 6: Types of Energy Sources
PPT-026-05
6
Electrical
Hydraulic
Pneumatic
Thermal
Chemical
Mechanical
Cord & Plug
Equipment
Other Types
List & Identify all Sources of Energy
Notes: Types of energy sources encompass the following. List and identify all sources toward which procedures and policies will be directed.
Electrical
Hydraulic
Pneumatic
Thermal
Chemical
Mechanical
Cord & Plug Equipment
Other Types

## Slide 7: Authorization
PPT-026-05
7
Any employee involved in the service or maintenance of any machine or equipment having potential for release of hazardous energy is authorized to Lock-out/Tag-out if he or she is adequately trained
Notes: The authorization to perform LOTO rests with,
Any employee
involved in the service or maintenance of
any machine or equipment
having a potential for release of hazardous energy
is authorized to Lock-out/Tag-out if he or she is adequately trained

## Slide 8: What Should be Done?
PPT-026-05
8
Appoint a “Program Administrator”
Determine what machines/equipment need to be locked/tagged out (e.g. by JHA/inspection/knowledge)
Purchase appropriate locks/tags
Notes: What should be done?
Appoint a “Program Administrator”
Determine what machines/equipment need to be locked/tagged out (e.g. by JHA/inspection/knowledge)
Purchase appropriate locks/tags

## Slide 9: What Should Be Done?
PPT-026-05
9
Develop a LOTO program
Determine status of employees (authorized,
affected, etc.)
Provide training
Implement program
Notes: Also,
Develop a LOTO program
Determine status of employees (authorized, affected, etc.)
Provide training
Implement program

## Slide 10: Program Responsibility
PPT-026-05
10
Responsibility should be given to a “program administrator” for:
  Lock acquisition
  Safe work procedures
  Training coordination
  Contractor coordination
  Assisting supervisors in implementation and enforcement of
  disciplinary actions for non-compliance
Notes: The responsibility of the program should be given to a “program administrator” for:
  Lock acquisition
  Safe work procedures
  Training coordination
  Contractor coordination
  Assisting supervisors in implementation and enforcement of disciplinary actions for non-compliance

## Slide 11: Program Responsibility
PPT-026-05
11
Conducting periodic inspections
Documenting changes in control
program as result of inspections
Assisting in development of
specific procedures
Maintaining program availability
for employees and interested
persons
Notes: This Administrator should also be responsible for,
Conducting periodic inspections
Documenting changes in the control program as a result of inspections
Assisting in the development of specific procedures and
Maintaining program availability for employees and interested persons
As part of the LOTO program, the Program Administrator may want to consider having the authorized person’s picture placed on their tags/locks so that the “owner” of the tag/lock can be easily identified if their name is not recognized.

## Slide 12: When to Apply LO/TO
PPT-026-05
12
Application of Lockout/Tagout is required:
  When servicing and/or maintaining
  machines or equipment
  If it is necessary to remove a guard or bypass safety device or interlock
  If an employee has the potential to be exposed to material being processed
  (point of operation) or the machine
  operating cycle
Notes: Apply the LOTO provisions,
  When servicing and/or maintaining machines or equipment,
  If it is necessary to remove a guard or bypass safety device or interlock,
  If an employee has the potential to be exposed to material being processed (point of operation) or the machine operating cycle

## Slide 13: OSHA Exception to LOTO
PPT-026-05
13
Maybe, provided above criteria is met
Minor tool changes/adjustments/other minor servicing activities taking place during normal production operations that are: routine, repetitive, and integral to the use of the equipment for production (provided alternative measures offering effective protection are used)
Could changing a drill bit qualify as an exception?
Notes: OSHA makes exceptions to the LOTO when all items can be satisfied.
Minor tool changes/adjustments/other minor servicing activities taking place during normal production operations that are: routine, repetitive, and integral to the use of the equipment for production (provided alternative measures offering effective protection are used)

## Slide 14: Exclusions
PPT-026-05
14
The LOTO Standard does not apply to:
Cord and Plug Electrical Equipment:
Plug has to be under the exclusive control of the
employee performing servicing or maintenance
Hot tap operations: Welding on transmission and distribution systems (water, gas, steam or petroleum products) when performed on pressurized pipelines, provided the employer demonstrates that:
– Continuity of service is essential
– Shutdown of system is impractical
– Documented procedures are followed
– Special equipment used to provide proven
effective protection for employees
Notes: Exclusions also exist where the LOTO standard does NOT apply:
Cord and Plug Electrical Equipment:
Plug has to be under the exclusive control of the employee performing servicing or maintenance
Hot tap operations: Welding on transmission and distribution systems (water, gas, steam or petroleum products) when performed on pressurized pipelines, provided the employer demonstrates that:
– Continuity of service is essential
– Shutdown of system is impractical
– Documented procedures are followed
– Special equipment used to provide proven effective protection for employees

## Slide 15: Authorized Devices
PPT-026-05
15
Shall be capable of withstanding the environment to which they are exposed for the maximum period of time that exposure is expected
Tag-out devices must be constructed and printed so that exposure to weather will not cause deterioration or the message to become illegible
Shall indicate the identity of the person applying the device
Notes: The LOTO requires authorized devices be applied to notify other workers the program in in effect. These devices:
Shall be capable of withstanding the environment to which they are exposed for the maximum period of time that exposure is expected
Tag-out devices must be constructed and printed so that exposure to weather will not cause deterioration or the message to become illegible
Shall indicate the identity of the person applying the device

## Slide 16: Documented Procedure for Every Machine
PPT-026-05
16
Not necessary if everything listed below exists:
Machine/equipment has no potential for stored or residual
energy or re-accumulation of stored energy after shut down
which could injure employees
Machine/equipment has single energy source readily
identified and isolated
Isolation and LOTO of that energy source will completely
de-energize and deactivate machine/equipment
Machine/equipment is isolated from that energy source and
locked out during servicing/maintenance
Notes: Documented procedures for every machine are not necessary if EVERYTHING listed below exists.
Machine/equipment has no potential for stored or residual energy or re-accumulation of stored energy after shut down which could injure employees
Machine/equipment has single energy source readily identified and isolated
Isolation and LOTO of that energy source will completely de-energize and deactivate machine/equipment
Machine/equipment is isolated from that energy source and locked out during servicing/maintenance

## Slide 17: Documented Procedure for Every Machine
PPT-026-05
17
Not necessary if all exist:
Single LOTO device will achieve a locked-out condition
LOTO device is under the exclusive control of the authorized
employee performing servicing/maintenance
Servicing/maintenance does not create hazards for others
The employer has had no accidents involving unexpected
activation/re-energization of machine/equipment being
serviced/maintained
Notes: Not necessary if all the following also exist:
Single LOTO device will achieve a locked-out condition
LOTO device is under the exclusive control of the authorized employee performing servicing/maintenance
Servicing/maintenance does not create hazards for others
The employer has had no accidents involving unexpected activation/re-energization of machine/equipment being serviced/maintained

## Slide 18: Authorized Employee
PPT-026-05
18
Person who locks or tags out machine
Suggestion: The Appendix of your LOTO Program should contain a list of Authorized Employees for the particular area/facility
Notes: An Authorized Employee is one who locks or tags out a machine.
Suggestion: The Appendix of your LOTO Program should contain a list of Authorized Employees for the particular area/facility

## Slide 19: Affected Employee
PPT-026-05
19
Employees whose job requires them to operate the machine or process on which maintenance or service is being performed
Need to be notified upon shutdown and start up
Notes: The Affected Employee are those whose job
Requires them to operate the machine or process on which maintenance or service is being performed
Need to be notified upon shutdown and start up

## Slide 20: Other Employee
PPT-026-05
20
An individual who may be in the area and affected by the shut down or start up of a machine (e.g. janitor).
Required to recognize when energy control procedures are being used,
Understand the purpose of the procedure, and
Understand the critical importance of not attempting to start up or use equipment that has been locked out or tagged out.
Notes: Other employees are those whose job may put them in an area whereby they could be affected by the shut down or start up of a machine.
Required to recognize when energy control procedures are being used,
Understand the purpose of the procedure, and
Understand the critical importance of not attempting to start up or use equipment that has been locked out or tagged out.

## Slide 21: Affected Work Station
PPT-026-05
21

## Slide 22: Individual Lockout
PPT-026-05
22
Shut down machine; power control off; lockout
Stored energy dissipated and then isolated
Engage controls for machine operation, verify OFF
Work may proceed
If shift changes, individual LOTO repeated by next shift
Notes: An individual Lockout sequence would include:
Shut down machine; power control off; lockout
Stored energy dissipated and then isolated
Engage controls for machine operation, verify OFF
Work may proceed
If shift changes, individual LOTO repeated by next shift

## Slide 23: Restoring Equipment to Service
PPT-026-05
23
Replace all guards and safety devices
Inspect work area to ensure all nonessential items have been removed and machine/equipment components are operationally intact
Vents and bleeders closed, blinds removed, blocks and tags removed
Employees notified and moved to safe area
Notes: Restoring Equipment sequences would also be included, e.g.
Replace all guards and safety devices
Inspect work area to ensure all nonessential items have been removed and machine/equipment components are intact
Vents and bleeders closed, blinds removed, blocks and tags removed
Employees notified and moved to safe area

## Slide 24: Restoring Equipment to Service
PPT-026-05
24
Each employee removes his or her lock
Machine re-started to ensure working properly/safely
Affected employees notified that machine/equipment back in service
Notes: Restoration of service also has its stages.
Each employee removes his or her lock
Machine re-started to ensure working properly/safely
Affected employees notified that machine/equipment back in service

## Slide 25: Group Lockout
PPT-026-05
25
Same as individual lockout except:
  Primary responsibility vested in authorized employee for set number of employees involved
  Provision for authorized employee to ascertain exposure status of individual group members
  When more than one crew, craft, department, etc. involved LOTO responsibility given to one authorized employee for coordination
  Each authorized employee affixes personal LOTO device to group LOTO device/lockbox when they begin work
Notes: A Group Lockout is the same as an individual lockout with the following exceptions:
  Primary responsibility vested in authorized employee for set number of employees involved
  Provision for authorized employee to ascertain exposure status of individual group members
  When more than one crew, craft, department, etc. involved LOTO responsibility given to one authorized employee for coordination
  Each authorized employee affixes personal LOTO device to group LOTO device/lockbox when they begin work

## Slide 26: Group Lockout Boxes
PPT-026-05
26
Notes: The slide shows variations of Group Lockout Boxes obtainable from vendors.

## Slide 27: Group Restoration to Service
PPT-026-05
27
Each “trade” - replace all guards and safety devices
Vents and bleeders closed, blinds removed, blocks and tags removed
Each employee removes his or her lock
Notes: Group restoration to service also includes:
Each “trade” - replace all guards and safety devices
Vents and bleeders closed, blinds removed, blocks tags removed
Each employee removes his or her lock

## Slide 28: Group Restoration to Service
PPT-026-05
28
Employees are notified and removed to a safe distance
Group Authorized Person ensures machine device operating properly/safely
Group Authorized Person notifies all personnel/affected employees that machine/equipment is back in service
Notes: During Group Restoration,
Employees are notified and removed to a safe distance
Group Authorized Person ensures machine device operating properly/safely
Group Authorized Person notifies all personnel/affected employees that machine/equipment is back in service

## Slide 29: Lock Removal Other Than Authorized Person
PPT-026-05
29
A situation may arise whereby a lock needs to be removed and the authorized person who put it in place is not on-site
Can be done as long as documented procedure is followed
At a minimum the procedure must include: (1) Verification by the employer that the authorized employee who applied the device is not on site;
(2) All reasonable efforts to contact the authorized employee to inform him or her that the lock has been removed; and
(3) The employee is definitely informed of the removal of the lock upon his or her return to work.
Notes: There are times when a situation necessitates the removal of a lock and the authorized employee who put that lock in place is not on-site. That individual’s lock can be removed provided a documented procedure is in place which, at a minimum, includes the items listed.
NOTE: Obviously, the "one person, one lock, one key" practice is the preferred means and is accepted across industry lines, but it is not the only method to meet the language of the standard. However, prior to the use of a master key method, specific procedures and training, meeting the §1910.147(e)(3) exception, must be developed, documented, and incorporated into your energy control program. Among the features essential to a compliant master key procedure is a reliable method to ensure that access to the master key will be carefully controlled by the employer such that only those persons authorized and trained to use the master key in accordance with the employer's program can gain access.

## Slide 30: Long Term Safety Lockout
PPT-026-05
30
Extended period of time:
Machine’s use discontinued or is no longer part of operation
Long term locks available for use by the responsible person
Notes: Some systems may be removed from service not to be replaced or awaiting replacement by newer equipment. Extended period lockouts may also be accommodated.
Machine’s use discontinued or is no longer part of operation
Long term locks available for use by the responsible person

## Slide 31: Unauthorized Removal
PPT-026-05
31
Consequences of unauthorized removal of LOTO devices:
Should be listed in the program (let all personnel know what actions occur if somebody removes or damages LOTO devices without authorization)
Example: “Only an Authorized Person can remove personal locks (list names and departments of authorized persons).
If a LOTO device is removed, damaged, or disabled, the responsible employee will receive disciplinary action pursuant to …….”
Notes: Your program should indicate the consequences of unauthorized removal of LOTO devices. These consequences
should be listed in the program (let all personnel know what actions occur if somebody removes or damages LOTO devices without authorization)
Example: “Only an Authorized Person can remove personal locks (list names and departments of authorized persons).
If a LOTO device is removed, damaged, or disabled, the responsible employee will receive disciplinary action pursuant to …….”

## Slide 32: Subject to Disciplinary Action
PPT-026-05
32
All involved parties for failure to implement LOTO (including supervisors)
Misuse of LOTO equipment
Contractors who fail to adhere
Notes: Indicate those actions subject to disciplinary action,
All involved parties for failure to implement LOTO (including supervisors)
Misuse of LOTO equipment
Contractors who fail to adhere

## Slide 33: Tags
PPT-026-05
33
Used if energy isolating
device not capable of being locked out
Tags should not be removed without authorization of the authorized person responsible for it
Tags must be legible and understandable by all employees
Notes: Tags are used if an energy isolating device is not capable of being locked out
Tags should not be removed without authorization of the authorized person for it
Tags must be legible and understandable by all employees

## Slide 34: Tags
PPT-026-05
34
Tags and their means of attachment must be made of materials that can withstand environmental conditions
Tags must be securely attached to energy isolating devices
Notes: Tags and their means of attachment must be made of materials that can withstand environmental conditions
Tags must be securely attached to energy isolating devices

## Slide 35: Training
PPT-026-05
35
1910.147 (c)(7)(i) = “The employer shall provide training to ensure that the purpose and function of the energy control program are understood by employees and that the knowledge and skills required for the safe application, usage, and removal of the energy controls are acquired by employees”
Notes: Training is covered in the standard at 1910.147 (c)(7)(i) = “The employer shall provide training to ensure that the purpose and function of the energy control program are understood by employees and that the knowledge and skills required for the safe application, usage, and removal of the energy controls are acquired by employees”

## Slide 36: Training-All Employees
PPT-026-05
36
Training Should Include:
  Purpose of LOTO program
  Use of the energy control program
  LOTO devices and plant specifics
  Rules and consequences of
  unauthorized removal of LOTO devices
Notes: Training should include:
  - Purpose of LOTO program
  - Use of the energy control program
  - LOTO devices and plant specifics
  - Rules and consequences of unauthorized removal of LOTO devices

## Slide 37: Training – Authorized Employees
PPT-026-05
37
Electrical
Hydraulic
Pneumatic
Thermal
Chemical
Mechanical
Cord & Plug
Equipment
Other Types
In Summary: List & Identify all Sources of Energy
Notes: Training for Authorized Employees should include the following for purposes of structuring their JHA (Job Hazard Analysis) and policies:
Electrical
Hydraulic
Pneumatic
Thermal
Chemical
Mechanical
Cord & Plug Equipment
Other Types

## Slide 38: Training Authorized Persons
PPT-026-05
38
In addition to basic LOTO training given to all employees, training for “Authorized Persons” should also include:
  When to implement LOTO
  Recognition of hazardous energy sources
  Type and magnitude of energy in workplace
  Returning equipment to service
  If questions on application–specific actions to be taken
Notes: In addition to basic LOTO training given to all employees, training for “Authorized Persons” should also include:
  When to implement LOTO
  Recognition of hazardous energy sources
  Type and magnitude of energy in workplace
  Returning equipment to service
  If questions on application–specific actions to be taken

## Slide 39: Retraining
PPT-026-05
39
Authorized and Affected persons is required when:
New equipment brought into the workplace
Change in job assignment
Changes in LOTO equipment
Periodic audit identifies need
Notes: Retraining of both, Authorized and Affected Persons is required when:
New equipment brought into the workplace
Change in job assignment
Changes in LOTO equipment
Periodic audit identifies need

## Slide 40: Periodic Inspection
PPT-026-05
40
Periodic inspection should be performed at least annually by an authorized employee other than the one(s) using the energy control procedure being inspected
Periodic inspections are conducted to correct deviations or inadequacies
“Certify” inspections done:
- Identify machine or equipment - Date of inspection - Person performing inspection - Employees included
Notes: Periodic inspection should be performed at least annually by an authorized employee other than the one(s) using the energy control procedure being inspected
Periodic inspections are conducted to correct deviations or inadequacies
“Certify” inspections were done by including:
- Identify machine or equipment
- Date of inspection
- Person performing inspection
- Employees included

## Slide 41: Testing/Positioning of Machines, Equipment, Components
PPT-026-05
41
In situations where LOTO devices must be temporarily removed from the energy isolating device and the machine/equipment has to be energized to test or position:
­ Clear the machine or equipment of tools and materials
­ Remove employees from the machine/equipment area
­ Remove the LOTO devices
­ Energize and proceed with testing/positioning
­ De-energize all systems and reapply energy control measures to continue servicing/maintaining
Notes: In situations where LOTO devices must be temporarily removed from the energy isolating device and the machine/equipment has to be energized to test or position:
­ Clear the machine or equipment of tools and materials
­ Remove employees from the machine/equipment area
­ Remove the LOTO devices
­ Energize and proceed with testing/positioning
­ De-energize all systems and reapply energy control measures to continue servicing/maintaining

## Slide 42: Contractors
PPT-026-05
42
Exchange LOTO procedures
Agree on procedures before work begins
Discipline of contractor and/or contractor employees for failure to use LOTO
Notes: Contractors may do work which interrupts production. Meet with contractors prior to work.
Exchange LOTO procedures
Agree on procedures before work begins
Discipline of contractor and/or contractor employees for failure to use LOTO

## Slide 43: Appropriate Posting
PPT-026-05
43
Notes: Areas which, through JHA and inspection, have been deemed LOTO locations, post accordingly.
Some facilities have created facility maps which indicate the locations and specific processes.
For each area, a procedure has been identified in a LOTO Procedure Manual.

## Slide 44: End Result
PPT-026-05
44
Due to OSHA and as a best practice, facilities should have a LOTO program in place where appropriate
Employees should receive LOTO training as appropriate and training should be documented
Employees need to understand when LOTO in use they should not attempt to remove or otherwise re-energize the machine
Notes: Due to OSHA and as a best practice, facilities should have a LOTO program in place where appropriate
Employees should receive LOTO training as appropriate and training should be documented
Employees need to understand when LOTO in use they should not attempt to remove or otherwise re-energize the machine

## Slide 45: Contact Information
PPT-026-05
45
Health & Safety Training Specialists
1171 South Cameron Street, Room 324
Harrisburg, PA 17104-2501
(717) 772-1635
RA-LI-BWC-PATHS@pa.gov
Like us on Facebook! - https://www.facebook.com/BWCPATHS
Notes: We invite you to contact us for more information on other free power point programs any free training at your location.

## Slide 46: Questions
PPT-026-05
46