## Slide 1: Scaffolds
Bureau of Workers’ Compensation
PA Training for Health & Safety (PATHS)
1926 Subpart L
Notes: 1926 Subpart L - Scaffolding
This presentation is designed to assist trainers conducting OSHA 10-hour Construction Industry outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of 1970 or for any standards issued by the U.S. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the U.S. Department of Labor.
This standard applies to all construction employees and employers who work on, under, or in close proximity to scaffolding and aerial lifts. Employees erecting and dismantling scaffolds also are covered.
General References:
 OSHA Publication 3150, A Guide to Scaffold Use in the Construction Industry:
www.osha.gov/Publications/osha3150.pdf
 OSHA Construction Scaffolding eCAT
www.osha.gov/SLTC/scaffolding_ecat/index.html

## Slide 2: What is a Scaffold?
An elevated, temporary work platform
Three basic types:
Supported scaffolds –
platforms supported by rigid,
load bearing members, such as
poles, legs, frames, & outriggers
Suspended scaffolds -- platforms suspended by ropes or other non-rigid, overhead support
Aerial Lifts -- such as “cherry pickers” or “boom trucks”
Notes: Supported scaffold - one or more platforms supported by outrigger beams, brackets, poles, legs, uprights, posts, frames, or similar rigid support.
Suspension scaffold - one or more platforms suspended by ropes or other non-rigid means from an overhead structure(s)
Aerial lifts – Vehicle-mounted devices used to get a worker to an elevated position, — referred to as “cherry pickers” or “boom trucks”

## Slide 3: Scaffolding
Designed by qualified person* and built loaded to design.
*by extensive knowledge, training,
and experience can solve problems
related to the subject matter.
Footing or anchorage must be sound, rigid, and capable of carrying the maximum intended load without displacement.
Must be capable of supporting at least 4 times the maximum intended load.
Notes: Designed by qualified person and built loaded to design.
Footing or anchorage of scaffolds must be sound, rigid, and capable of carrying the maximum intended load without displacement.
Must be capable of supporting at least 4 times the maximum intended load.

## Slide 4: Types of Scaffolds
There are many types of scaffolds for many types of different uses:
  Bricklayer’s Square Scaffolding
  Window-Jack Scaffolds
Scaffolds are also made out of different materials, but are typically found made out of metal or wood.
All have different OSHA regulations.
Notes: There are many types of scaffolds for many types of different uses
  Bricklayer’s Square Scaffolding
  Window-Jack Scaffolds
Scaffolds are also made out of different materials, but are typically found made out of metal or wood.
All have different OSHA regulations

## Slide 5: Scaffolding
Competent person* must inspect a scaffold before each work shift and after anything happens that could affect the structure.
Competent person* should be trained in scaffold safety.
Competent person* must supervise if a scaffold is assembled, changed, moved, or taken apart.
* Capable of identifying existing and predictable hazards and has authorization to take prompt measures to eliminate them.
Notes: With scaffolding, a Competent Person must inspect a scaffold before each work shift and after anything happens that could affect the structure.
Competent person* should be trained in scaffold safety.

## Slide 6: Competent Person
Person capable of identifying and promptly correcting hazards
Determines if it’s safe to work on a scaffold during storms or high winds
Trains workers to recognize hazards
Selects qualified workers to conduct work
Notes: A Competent Person as defined by relative OSHA regulations:
Person capable of identifying and promptly correcting hazards
Determines if it’s safe to work on a scaffold during storms or high winds
Trains workers to recognize hazards
Selects qualified workers to conduct work

## Slide 7: Frame Scaffold Components
Frames
Locking Devices
Cross, Horizontal and Diagonal Braces
Base Plates and Screw jacks
Putlogs
Casters
Platform Planks
Guard Rails and Gates
Ladders and Stair Units
Side and End Brackets
Hoisting Arms
Notes: Frame scaffolding is the most common type of scaffolding. It is also the easiest and simplest type of scaffolding to erect. Frame scaffolding can be applied either to the interior or exterior of a structure. There are many components in frame scaffolding.
Frames
Locking Devices
Putlogs
Cross, horizontal and diagonal braces
Base plates and Screw Jacks
Casters
Platform Planks
Guard Rails and Gates
Ladders and Stair Units
Hoisting Arms
Side and End Brackets
Every scaffold manufacturer has a complete product line of these and other components and accessories. Always refer to the manufacturer’s product manual or company representative if you have any questions regarding scaffolding components and their proper use.

## Slide 8: Frames
Frames come in many styles and sizes.
Each offers the user a variety of configuration possibilities to meet their needs
Notes: Frames come in many styles and sizes. Each type offers the user a variety of configuration possibilities to meet their needs. Read the manufacturer’s manual for more detailed information about the individual frame specifications.

## Slide 9: Scaffold Erection
Scaffolds can only be erected, moved, dismantled or altered under the supervision of a competent person
Competent person selects & directs these workers and determines the feasibility of fall protection
Notes: 1926.451(f)(7)
Activities must be performed by experienced and trained employees selected by the competent person.
1926.451(e)(9) & (g)(2)
When erecting and dismantling supported scaffolds, the competent person must determine the feasibility of providing a safe means of access and fall protection for these operations.
1926.452(c)(6)
Scaffolds over 125 feet high above the base plates must be designed by a registered professional engineer and constructed and loaded per the design.

## Slide 10: Hazards
Employees working on scaffolds are exposed to these hazards:
Falls from elevation – caused by slipping, unsafe access, and the lack of fall protection
Struck by falling tools/debris
Electrocution – from overhead power lines
Scaffold collapse - caused by instability or overloading
Bad planking giving way
Notes: About 2 of every three construction workers (2.3 million) work on scaffolds frequently.
Protecting these workers from scaffold-related accidents would prevent 4,500 injuries and 50 deaths every year, at a savings of $90 million in workdays not lost.
See the Scaffolding Technical Links page - www.osha.gov/SLTC/scaffolding/index.html

## Slide 11: Scaffolding - Safety
Power lines: Keep scaffolds 10 feet or more from power lines (or 3 feet, if lines are less than 300 volts), unless you are sure the power lines are de-energized.
Weather: Cannot work on a scaffold in high winds or a storm unless competent person says it is safe and you use personal fall-arrest or a windscreen. (If you use a screen, scaffold must be secured against the expected wind force).
Must not work on a scaffold that has ice or snow on it except to get ice or snow off the scaffold.
Notes: Set-up precautions look at power lines and the weather.
Power lines: Keep scaffolds 10 feet or more from power lines (or 3 feet, if lines are less than 300 volts), unless you are sure the power lines are de-energized.
Weather: Cannot work on a scaffold in high winds or a storm unless competent person says it is safe and you use personal fall-arrest or a windscreen. (If you use a screen, scaffold must be secured against the expected wind force).
Must not work on a scaffold that has ice or snow on it except to get ice or snow off the scaffold

## Slide 12: Overhead Power Lines
The possibility of electrocution is a serious consideration when working near overhead power lines
Check the clearance distances listed in the standard
Notes: 1926.451(f)(6)
The standard requires specific clearance distances, see 1926.451(f)(6) for a table listing those distances.
Scaffolds may be closer to power lines than specified where the clearance is necessary to perform work, but only after the utility company, or electrical system operator, is notified of the need to work closer and they de-energized or relocate the lines, or installed protective coverings to prevent contact with the lines.

## Slide 13: Wind Force
Notes: There are many factors to consider in the design and erection of a scaffold. None is more important that wind force, especially in the erection of an enclosed scaffold. For example, on an enclosed scaffold with a horizontal length of 100 feet and a vertical height of 100 feet, there is 10,000 square feet of surface area. A wind force of 50 MPH will exert a force of about 12.3 pounds per square foot on the scaffold. This means that the total force exerted on the scaffold would be equal to 123,000 pounds, which is exceedingly more force than would be applied if the scaffold work platforms were loaded down with materials. Wind forces can easily push the scaffold against or pull it away from the structure. Either result could be devastating.
General Safety Guidelines:
1. Check to ensure that all ties are positive type ties.
2. Check to ensure that all ties are located as close as possible to the posts.
3. Check to ensure that all frames are securely fastened together.
4. Check to ensure that the material used to enclose the scaffold is fastened to the frame and not the cross braces.
5. Check to ensure that the scaffold is properly ventilated to prevent toxic air.
6. If number 9 wire is used, check to ensure the ties have at least four strands.
7. Check ties at regular intervals, especially after a heavy wind.
8. Additional horizontal diagonal bracing, and additional tie-in locations will be necessary.

## Slide 14: Avoid the Main Scaffold Hazards
Falls from elevation
Bad planking
Scaffold collapse
Electrocution
Getting struck by falling tools or debris
Notes: Avoid the hazards listed!

## Slide 15: Fall Hazards
Falls may occur:
While climbing on or off the scaffold
Working on unguarded scaffold platforms
When scaffold platforms or planks fail
Notes: Falling while working on/from a scaffold is something that needs to be considered by all involved.
Workers need to be protected so that falls don’t occur:
While climbing on or off the scaffold
Working on unguarded scaffold platforms
When scaffold platforms or planks fail

## Slide 16: Protecting Workers from Falls
If a worker on a scaffold can fall more than 10 feet, protect them by:
Guardrails, and/or
Personal Fall Arrest Systems (PFAS)
Notes: Reference 1926.451(g)
Personal fall arrest system - a system used to arrest an employee’s fall. It consists of an anchorage, connectors, and a body harness and may include a lanyard, deceleration device, lifeline, or combinations of these.
The type of fall protection required depends on the kind of scaffold being used.

## Slide 17: Guardrails
Install along open sides & ends
Front edge of platforms not more than 14 inches from the work, unless using guardrails and/or PFAS
Top rails - 38 to 45 inches tall
Midrails halfway between toprail and platform
Toeboards at least 3-1/2 inches high
Notes: Reference 1926.451(g)(1), (g)(4), (b)(3), and Appendix A, paragraph 1d.
38 inch minimum guardrail height where guardrail is primary fall protection.
36 inch minimum guardrail height where fall arrest systems are primary fall protection.
Protect from falling between the top rail and surface, by using midrails, screens or mesh.
Protective barriers must be strong enough to support a falling employee. Wood, chain and wire rope may be used for top rails and midrails.
Top rails - 36-48 inches tall when using the crossbracing as the top rail
When crossbracing is used as a midrail, it must be between 20 and 30 inches above the work platform.
Guardrails are not required:
• when the front end of all platforms is less than 14 inches from the face of the work
• when outrigger scaffolds are three inches or less from the front edge
• when employees are plastering and lathing 18 inches or less from the front edge

## Slide 18: Personal Fall Arrest Systems
Short title: PFAS
You must be trained how to properly use PFAS
PFAS include anchorage, lifeline and body harness
Notes: Reference 1926.502(d) and 1926.503
Personal Fall Arrest Systems = body harnesses and their components, such as anchorage points, lifelines, “D” rings, and snap hooks.
What will my personal fall arrest system do to protect me?
A personal fall arrest system places the employee into a body harness that is fastened to a secure anchorage so that he/she cannot fall. Body belts are not acceptable as personal fall arrest systems. A few key requirements:
There should be no free fall more than 6 feet.
There should be prompt rescue after a fall.
Inspect PFAS’s prior to each use.
Don’t use PFAS’s until they’ve been inspected by a competent person.
A competent person must determine the feasibility and safety of providing fall protection for employees erecting or dismantling supported scaffolds.

## Slide 19: Fall Protection Requirements
  Can use PFAS instead of guardrails on some scaffolds
  Use PFAS & guardrails on suspension scaffolds
  Use PFAS on erectors and dismantlers where feasible
The ends of this scaffold are not properly guarded
Notes: Reference 1926.451(g)
    What fall protection will I need when working on scaffolds?
    Boatswains’ chair, catenary scaffold, float scaffold, needle beam scaffold, ladder jack scaffold – personal fall arrest system.
    Single-point or two-point adjustable scaffold – personal fall arrest system and a guardrail system.
    Crawling board (chicken ladder) – personal fall arrest system, guardrail system or by a three-fourth inch diameter grabline or equivalent handhold securely fastened beside each crawling board.
    On a walkway within a scaffold – guardrail system installed within 9 ½ inches of and along at least one side of the walkway
    On a supported scaffold when performing overhand bricklaying operations – personal fall arrest system or guardrail system on all open sides and ends of the scaffold.
    For all other scaffolds, a personal fall arrest system or a guardrail system

## Slide 20: Falling Object Protection
    Wear hardhats
    Barricade area below scaffold to forbid entry into that area
    Use panels or screens if material is stacked higher than the toeboard
    Build a canopy or erect a net below the scaffold that will contain or deflect falling objects
Notes: Reference 1926.451(h)(1) & (2) & (3)
How am I protected from falling objects when I am working on a scaffold?
The major protection is to always wear a hardhat. In addition, when there is the danger of falling hand tools, debris, and other small objects, the employer must install toeboards, screens or guardrail systems above the worker on a scaffold, or through the erection of debris nets, catch platforms, or canopy structures that contain or deflect the falling objects.
When the potential falling objects are too large to be held by toeboards, screens or guardrail systems, the employer must place such objects away from the edge of the surface from which they could fall, and must secure those materials as necessary to prevent their falling.
Workers on scaffolds must be aware of employees working below them, who are in danger from objects falling from the scaffold. Where this danger exists, the employer must erect a barricade to keep employees from working below the scaffold, or must place a toeboard or an edging along the edge of the platform.

## Slide 21: Scaffold Support Examples
Good Support with:
Mud sills and
Base plate
Inadequate support –
in danger of collapse?
Notes: Cinder blocks or other similar materials should not be used to support a scaffold because they could be crushed.
Any time there is inadequate support, improper construction or a shift in the components of the scaffold (including the base upon which the structure is built), there is danger of collapse.

## Slide 22: Base Plates & Screw Jacks
These provide a solid foundation for the scaffolding.
Improper use could cause the scaffold to collapse.
Base plates should always be used, even on concrete.
Notes: Before the walls of a building can be erected a solid foundation must be laid. This is also the case with a scaffold. Base plates and screw jacks serve as the foundation of the scaffold. Improper preparation of the surface where these foundation components are placed, along with their improper use can cause the scaffold to collapse. Base plates should always be used, even on concrete.

## Slide 23: Safe Scaffolds
Essential Elements of Safe Scaffold Construction:
Use appropriate scaffold construction methods
Proper scaffold access
Properly use a competent person
Notes: Essential Elements of Safe Scaffold Construction:
Use appropriate scaffold construction methods
Proper scaffold access
Properly use a competent person

## Slide 24: Scaffold Platform Construction
Platforms must:
  Be fully planked or decked with no more than 1 inch gaps
  Be able to support its weight & 4 times maximum load
  Be at least 18 inches wide
This is not a properly
constructed scaffold
Notes: Reference 1926.451(b) and (a)
How wide does the work area need to be on scaffolding?
Each scaffold platform and walkway must be at least 18 inches wide.
When the work area is less than 18 inches wide, guardrails and/or personal fall arrest systems must be used.
Employees on a walkway located within a scaffold must be protected by a guardrail system installed within 9 1/2 inches of and along at least one side of the walkway.
Planking should be graded and marked as scaffold planking.

## Slide 25: Scaffold Platform Construction
    No large gaps in front edge of platforms
    Each abutted end of plank must rest on a separate support surface
    Overlap platforms at least 12 inches over supports, unless restrained to prevent movement
Planks not properly overlapped
Notes: Reference 1926.451(b)
Front edge of all platforms
- No more than 14" from the face of the work
- 3" from the face for outrigger scaffolds
- 18" from the face for plastering and lathing operations
Platforms 10' and less to extend at least 6" but not more than 12" past support unless designed and installed and/or guarded properly
Platforms greater than 10' no more than 18" past support unless designed and installed and/or guarded properly

## Slide 26: Platform Planks
Provide surface from which user can work and store materials.
Can be obtained from lumber yard or scaffold dealer.
Plywood, steel, aluminum, etc
Notes: Platform planks provide a surface from which the user can work and store materials. They can be obtained from a lumber yard or a scaffold dealer. Plywood, steel, and aluminum are also used as platform planking. Whichever type is used, it must comply with current scaffolding lumber standards and manufacturer’s recommendations.

## Slide 27: Lumber Grading
Bureau of Workers’ Compensation
PA Training for Health & Safety (PATHS)
American Lumber Standards Committee established associations that are approved to grade species of lumber
Dense Industrial 65 Scaffold Plank
Notes: The American Lumber Standards committee has established associations that are approved to grade species of lumber. They are the: SPIB (Southern Pine Inspection Bureau), WCLIB (West Coast Lumber Inspection Bureau), NLGA (National Lumber Grading Authority), and WWPA (Western Wood Products Association).
There are several different species that can be used. Each approved association has its own grading criteria for the species in its area. Consult the approved grading association for the minimum grade by species for your area. The Southern Pine “DI65” and the WCLB Douglas Fir “Select Structural” are the most commonly used species.

## Slide 28: Plank Testing
In addition to grading wood planks used in scaffolding, planks are tested.
Weight requirement for a plank = 250 pounds for one person.
OSHA states scaffolding planks shall not deflect more than 1/60 of their span when loaded.
When in doubt, discard plank.
Notes: In addition to grading wood planks used in scaffolding, planks are tested.
Weight requirement for a plank = 250 pounds for one person.
OSHA states scaffolding planks shall not deflect more than 1/60 of their span when loaded.
When in doubt, discard plank.

## Slide 29: Scaffold Platform Construction
  No paint on wood platforms
  Use scaffold grade wood
  Fully planked between front upright and guardrail support
  Component pieces used must match and be of the same type
  Erect on stable and level ground
  Lock wheels and braces
Notes: Reference 1926.451(b)
Identification paint may be used on the edges of the wooden planks.
Do not use dissimilar metals in scaffold assembly

## Slide 30: Scaffold Height
  The height of the scaffold should not be more than four times its minimum base dimension unless guys, ties, or braces are used
5’
20’
Notes: The height of a scaffold needs to be taken into consideration when planning for its construction and placement.

## Slide 31: Scaffold Ties
All scaffolds with height to base ratio of more than 4 to 1 must be secured to the structure or guyed to prevent tipping over.
Scaffold tie purpose = bracing scaffold.
All ties should provide compressive as well as tensile resistance to any lateral forces acting on the scaffold
Notes: All scaffolds with a height to base ratio of more than four to one must be secured to the structure or guyed to prevent the scaffold from tipping over. The ties should be repeated every 30 feet horizontally and vertically at 20 feet for scaffolds 3 feet wide or less, or 26 feet for scaffolds wider than 3 feet.
A scaffold tie has the purpose of bracing the scaffold leg to prevent bowing. As a result all ties should provide compressive and tensile resistance to any lateral forces acting on the scaffold. In other words, the leg must be braced for “push and pull”, so that the scaffold cannot move into or away from the building.
There are many ways in which a scaffold can be properly secured to a building or structure. Special consideration must also be given to any scaffold that is enclosed by tarps or poly. Tremendous wind forces may be imposed on the scaffold, this would mean that the ties would need to be stronger as well.

## Slide 32: Platform Ends
Each end of a platform, unless cleated or otherwise restrained by hooks, must extend over its support by at least 6 inches
No Cleats
Notes: 1926.451(b)(4) and 1926.451(b)(5)
Each platform end 10 feet or less shall not extend over its support more than 12 inches unless the platform is designed and installed so that the cantilevered portion of the platform is able to support employees and/or materials without tipping, or has guardrails which block employee access to the cantilevered end.
Each platform end more than 10 feet in length shall not extend over its support more than 18 inches, unless it is designed and installed so that the cantilevered portion of the platform is able to support employees without tipping, or has guardrails which block employee access to the cantilevered end.

## Slide 33: Supported Scaffolds
  Platforms supported by legs, outrigger beams, brackets, poles, uprights, posts, & frames
  Restrain from tipping by guys, ties, or braces
  Scaffold poles, legs, posts, frames, and uprights must be on base plates and mud sills or other firm foundation
This support is not adequate!
Notes: Reference 1926.451(c)
Framed squares made of metal or wood, usually assembled on site
The structural members: poles, legs, posts, frames, and uprights must be plumb and braced to prevent swaying and displacement.
Supported scaffolds with a height to base width ratio of more than 4:1 must be restrained by guying, tying, bracing, or an equivalent means.
How can one prevent supported scaffolding from tipping?
Either the manufacturers’ recommendation or the following placements must be used for guys, ties, and braces:
• Install guys, ties, or braces at the closest horizontal member to the 4:1 height and repeat vertically with the top restraint no further than the 4:1 height from the top.
• Vertically—every 20 feet or less for scaffolds less than three feet wide; every 26 feet or less for scaffolds more than three feet wide.
• Horizontally—at each end; at intervals not to exceed 30 feet from one end.

## Slide 34: Proper Scaffold Access
Provide access when scaffold platforms are more than 2 feet above or below a point of access
Permitted types of access:
Ladders, such as portable, hook-on, attachable, stairway type, and built-ins
Stair towers
Ramps and walkways
May use building stairs and come out window
Notes: 1926.451 (e)
Access requirements for employees erecting and dismantling supported scaffolds -- Must have a safe means of access provided when a competent person has determined the feasibility and analyzed the site conditions.
Direct access to or from another surface shall only be used when the scaffold is not more than 14 inches horizontally and 24 inches vertically from the other surface.
Portable, Hook-on, and Attachable Ladders - position to not tip the scaffold.
Hook-on and Attachable Ladders - must be specifically designed for the type of scaffold with which they are used.
Ramps and Walkways - must have guardrails which comply with [1926.502(b)] 1926 Subpart M if more than 6 feet above lower levels.
Stairway-type Ladders and Stair Towers - bottom step no more than 24 inches above the level on which the scaffold is supported.
Built-in Scaffold Ladders - must be specifically designed and constructed for use as ladder rungs.

## Slide 35: Scaffold Access
    No access by crossbraces
    When using ladders, bottom rung no more than 24 inches high
    Can use some end frames
    Can access from another scaffold, structure or hoist
End Frame
Do not access
by crossbraces
Notes: Reference: OSHA 29 CFR 1926.451(e)

## Slide 36: Ladders and Stair Units
Ladder and stair units allow for ease of access to scaffold work areas.
They are manufactured in many styles to suit the user’s need.
Notes: Ladders and stair units allow ease of access to scaffold work areas. They are manufactured in many styles to suit the user’s need. They can be installed on the interior or exterior of the scaffold.

## Slide 37: Suspension Scaffolds
Platforms suspended by ropes or wires. Rope must be capable of supporting 6 times the load
Train to recognize hazards
Secure/tie to prevent swaying
Support devices must rest on
surfaces that can support four
times the load
Competent person:
Evaluate connections to ensure
Supporting surfaces can support load
Inspect ropes for defects before shift
PFAS must have anchors independent of the scaffold support system
Notes: 1926.450(b), 1926.451(a), (d), and (g)
Each suspension rope, including connecting hardware, used on non-adjustable suspension scaffolds shall be capable of supporting, without failure, at least 6 times the maximum intended load applied or transmitted to that rope.

## Slide 38: Moving Scaffolds
Employees can’t be on a moving scaffold unless:
  Surface is level
  Height to base ratio is 2 to 1
  Outriggers are installed on both sides of scaffolds
Employees can’t be on scaffold part beyond the wheels
Competent person must be on site to supervise
Notes: 1926.451(f)(5)
Scaffolds shall not be moved horizontally while employees are on them, unless they have been designed by a registered professional engineer specifically for such movement or, for mobile scaffolds, where the provisions of 1926.452(w) are followed.
1926.452(w)(6)
Employees cannot ride on scaffolds unless::
The surface on which the scaffold is being moved is within 3 degrees of level, and free of pits, holes, and obstructions;
The height to base width ratio of the scaffold during movement is two to one or less, unless the scaffold is designed and constructed to meet or exceed nationally recognized stability test requirements
Outrigger frames, when used, are installed on both sides of the scaffold;
When power systems are used, the propelling force is applied directly to the wheels, and does not produce a speed in excess of 1 foot per second;
No employee is on any part of the scaffold which extends outward beyond the wheels, casters, or other supports.

## Slide 39: Fatal Fact-Moving a Lift
Employee was operating an aerial lift, with an extendable boom rotating work platform
The boom was fully extended and the machine apparently ran over some bricks, causing the boom to flex or spring, throwing the employee from the basket
The employee fell 37 feet to a concrete surface
Notes: Unfortunately workers are injured every year through acts such as this. Employees need to ensure they are working safely and not taking shortcuts that can lead to injuries or even death.

## Slide 40: NO Shore or Lean-to Scaffolds!
Shore scaffold supported scaffold which is placed against a building or structure and held in place with props
Lean-to scaffold supported scaffold which is kept erect by tilting it toward and resting it against a building or structure
Notes: 1926.451(f)
Shore scaffold - a supported scaffold which is placed against a building or structure and held in place with props
Lean-to scaffold - a supported scaffold which is kept erect by tilting it toward and resting it against a building or structure
Do not load scaffolds or scaffold components in excess of their maximum intended loads or rated capacities, whichever is less.

## Slide 41: Using Scaffolds
Don’t work on snow or ice covered platforms or during storms or high winds
Use tag lines on swinging loads
Protect suspension ropes from heat & acid
A covered scaffold has special wind load considerations
Notes: Reference 1926.451(f)

## Slide 42: Fatal Fact-Ice & No Guardrails
Laborer was working on the third level of a tubular welded frame scaffold which was covered with ice and snow
The scaffold was not fully decked, there was no guardrail and no access ladder
The worker slipped and fell head first 20 feet to the pavement below
Notes: Here is yet another incident that caused a fatality – another worker who won’t be coming home tonight!

## Slide 43: Overhand Bricklaying
From Supported Scaffolds:
A guardrail or personal fall arrest system is required on all sides except the side where the work is being done.
Notes: 1926.451(g)(1)(vi)

## Slide 44: Scaffold Inspection
Competent person inspects scaffolds for visible defects before each shift and after any alterations
Defective parts must be immediately repaired
Deformed bearer
Notes: 1926.451(f)(3), 1926(f)(4)
A competent person must inspect scaffolds and scaffold components for visible defects before each work shift, and after any occurrence which could affect a scaffold's structural integrity.
Any part of a scaffold damaged or weakened such that its strength is less than that required shall be immediately repaired or replaced, braced to meet those provisions, or removed from service until repaired.

## Slide 45: Locking Devices
Locking device necessary when frame requires more than one level.
Secures frames as they are stacked on one another.
Notes: When a frame scaffold requires more than one level, a locking device such as a coupling pin is needed to secure the frames as they are stacked on top of one another. Other types of locking devices include the rivet and hair pin, pig tail pin, spring pin, toggle pin, etc. Locking devices are also used to secure scaffold braces.

## Slide 46: Casters
Primary use is in the erection of rolling tower scaffolds.
Typically made of rubber or steel in varying diameters and equipped with a locking device.
Notes: The primary use of casters is in the erection of rolling tower scaffolds. They are made of rubber or steel wheels in varying diameters and are equipped with a locking device. They are used with specially designed base frames for use in interior structures.

## Slide 47: Casters-Safety Precautions
Caster brakes should be set before an employee gets on a scaffold.
If no brakes are available, another employee should be in position to secure the scaffold.
Notes: Caster brakes should be set before an employee gets on a scaffold.
If no brakes are available, another employee should be in position to secure the scaffold.

## Slide 48: Braces
Strength and stability are important considerations when planning, erecting, and using scaffold.
Cross, horizontal and diagonal braces used to meet this requirement.
Notes: Strength and stability are important considerations when planning, erecting, and using a scaffold. Cross, horizontal and diagonal braces are used to meet this requirement. Ties are also used for this purpose. Cross braces are available in various lengths, and must be sized for the height of the frame. Horizontal braces are used where additional lateral rigidity is required (such as on a rolling tower).

## Slide 49: Putlogs
Scaffolds may be erected in areas where there are obstructions or openings (putlogs used)
Sometimes called a truss
Provide an excellent surface
for platforms
Care must be taken not to exceed load
Refer to Operator’s Manual for load capacities
Notes: A scaffold may have to be erected at a location where there are obstructions or openings. Putlogs, sometimes called a truss, are an inexpensive way of overcoming these difficulties. They also provide an excellent surface for platforms. Although this scaffold component is quite useful, care must be taken not to exceed load capacities. Always refer to the manufacturer's manual for load capacities.

## Slide 50: Brackets
Side and end brackets used to extend length or width of scaffold.
Expand work surface.
Should never be used for storage of work materials or equipment.
Notes: These components are used to extend the length of width of a scaffold. They expand the work surface and should never be used for the storage of work materials or equipment. They are also not to be used on rolling tower scaffolds (unless overturning forces are compensated for).

## Slide 51: Hoisting Arms
Hoisting arms = take materials and equipment to work platform of a scaffold.
Are easily installed and provide efficient means of transporting equipment
Notes: Getting materials and equipment to the work platform of a scaffold is the purpose of hoisting arms.
They are easily installed and provide as efficient means of transporting equipment.

## Slide 52: Training Requirements
    Train employees on scaffold hazards and procedures to control the hazards
    The training must include:
    Nature of electrical, fall,
    and falling object hazards
    How to deal with electrical
    hazards and fall protection
    systems
    Proper use of the scaffold
    Scaffold load capacities
Retrain as necessary
Notes: Reference 1926.454
Employees who work on a scaffold must be trained by a person qualified to recognize the hazards associated with the type of scaffold used and to understand the procedures to control and minimize those hazards. The training must include fall hazards, falling object hazards, electrical hazards, proper use of the scaffold, and handling of materials.
A competent person must train all employees who erect, disassemble, move, operate, repair, maintain, or inspect scaffolds. Training must cover the hazards, the correct procedures for erecting, disassembling, moving, operating, repairing, inspecting, and maintaining the type of scaffold in use. 1926.454(b)
Appendix D provides a guide to other recommended topics such as PPE, access, and guys, ties, braces and parts inspection which should be used to train scaffold erectors and dismantlers.
Retrain when:
Changes at the worksite present a new hazard
Changes in the types of scaffolds, fall protection, falling object protection, or other equipment present a new hazard
An employee's work with scaffolds indicates the need

## Slide 53: Training Erectors
Train employees involved in erecting, disassembling, moving, operating, repairing, maintaining, or inspecting a scaffold to recognize its hazards and the correct procedures to use
Notes: 1926.454(b) 1926.454 (c)
The training shall also include the design criteria, maximum intended load-carrying capacity and intended use of the scaffold
When the employer has reason to believe that an employee lacks the skill or understanding needed for safe scaffolding work, the employer shall retrain that employee

## Slide 54: Scaffolding
General Requirements
Must be maintained in a safe condition.
Must not be altered or moved horizontally while in use.
Should not be loaded in excess of the working load for which they are intended.
Materials hoisted onto a scaffold must have a tag line.
Notes: Scaffolding
Must be maintained in a safe condition.
Must not be altered or moved horizontally while in use.
Should not be loaded in excess of the working load for which they are intended.
Materials hoisted onto a scaffold must have a tag line.

## Slide 55: Scaffolding
General Requirements
Timbers, wood, nails and bolts must be adequate size.
All planking and platforms must be overlapped (by at least 12 inches).
An access ladder or equivalent safe access must be provided.
Tools, materials and debris must not be allowed to accumulate on scaffolding.
Notes: Timbers, wood, nails and bolts must be adequate size.
All planking and platforms must be overlapped (by at least 12 inches).
An access ladder or equivalent safe access must be provided.
Tools, materials and debris must not be allowed to accumulate on scaffolding

## Slide 56: Summary
Remember to:
Use appropriate scaffold construction methods
Erect, move, or alter scaffold properly
Protect from falling objects or tools
Ensure stable access
Use a competent person
Train on scaffold construction and the hazards involved with scaffolds
Inspect scaffold before each shift and after alterations
Determine fall protection requirements
Notes: General References:
 OSHA Publication 3150, A Guide to Scaffold Use in the Construction Industry:
www.osha.gov/Publications/osha3150.pdf
 OSHA Construction Scaffolding eCAT
www.osha.gov/SLTC/scaffolding_ecat/index.html
Other standards that apply to scaffolds
-- the responsibility to initiate and maintain programs (1926.20(b)(1))
-- exposures to dusts and chemicals (1926.33,1926.55,1926.59,1926.62, & 1926.1101)
-- hand and power tools (1926.300 -.307)
-- electrical (1926.400 -.449)
-- personal fall arrest systems (1926.502)
-- ladders (1926.1050 -.1060)

## Slide 57: Contact Information
Health & Safety Training Specialists
1171 South Cameron Street, Room 324
Harrisburg, PA 17104-2501
(717) 772-1635
RA-LI-BWC-PATHS@pa.gov
Like us on Facebook! - https://www.facebook.com/BWCPATHS
Notes: We invite you to contact us for information on other free training available.

## Slide 58: Questions

## Slide 59: Bibliography
29 CFR 1910.28 Safety Requirements for
Scaffolding
29 CFR 1910.29 Manually Propelled Mobile Ladder
Stands and Scaffolds (Towers)
29 CFR 1926.451 General Requirements (Scaffolds)