## Slide 1: Process Safety Management of Highly Hazardous & Explosive Chemicals
29CFR1910.119
Simple Keys to Compliance

## Slide 2: Objectives
Define what is PSM and who is covered by the standard
List the elements of the PSM standard

## Slide 3: What Is Process Safety Management?
PSM:
  Addresses the management of Highly Hazardous Chemicals (HHC)
  Integrates
    Technology
    Operating Procedures
    Standard management protocols

## Slide 4: Why Did OSHA Develop PSM?
  Past Disasters
  Current Disasters
  Perceived Weakness in PSM Program

## Slide 5: Why Did OSHA Develop PSM?
Bhopal, India (1984)
  2,000 deaths Isocyanate release
Pasadena, TX (1989)
  23 deaths, 132 injuries Petroleum explosion
Cincinnati, OH (1990)
  2 deaths Explosion
Sterlington, LA (1991)
  8 deaths, 128 injuries Chemical release

## Slide 6: Why Did OSHA Develop PSM?
In 1991, OSHA and EPA respectively, Released the Standards, PSM & RMP that Applies to Those Companies that are Affected by The Standards.

## Slide 7: Why Did OSHA Develop PSM?
Process Safety Management is a regulation, promulgated by OSHA, intended to prevent an incident like the 1984 Bhopal Disaster
And…to Prevent Release of:
  Toxic,
  Reactive,
  Flammable, or
  Explosive chemicals

## Slide 8: Not Only PSM, But RMP
A great many industrial facilities must comply with OSHA's Process Safety Management (PSM) regulations as well as the CAA 112(r) EPA Risk Management Program (RMP) regulations (Title 40 CFR Part 68).

## Slide 9: PSM vs. RMP - What’s the Difference?
RMP-Like Sara Title III
  Protects the Community
  Protects the General Public Around the Facility
  Protects Adjacent Facilities Such as Schools & Hospitals
PSM - Like HAZCOM
  Protects the Workforce
  Protects Contractors
  Protects Visitors to the Facility
  Basically Protects the Workplace

## Slide 10: The Standard Was Promulgated in 1991 - Is it Working?

## Slide 11: The Standard Was Promulgated in 1991 - Is it Working?
BP Products Texas City - March 2005
  15 Workers Killed
  170 Injured
  Major Property Damage
  $50.6 Million in Fines

## Slide 12: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response
Incident Investigation
Compliance Audits
Trade Secrets

## Slide 13: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Process Hazard Analysis
Management of Change
Operating Procedures
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response
Incident Investigation
Compliance Audits
Trade Secrets

## Slide 14: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response
Incident Investigation
Compliance Audits
Trade Secrets

## Slide 15: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response
Incident Investigation
Compliance Audits
Trade Secrets

## Slide 16: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response
Incident Investigation
Compliance Audits
Trade Secrets

## Slide 17: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response
Incident Investigation
Compliance Audits
Trade Secrets

## Slide 18: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response
Incident Investigation
Compliance Audits
Trade Secrets

## Slide 19: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Pre-Start up Safety Review
Hot Work Permit
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response

## Slide 20: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Pre-Start up Safety Review
Hot Work Permit
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response

## Slide 21: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Pre-Start up Safety Review
Hot Work Permit
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response

## Slide 22: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Pre-Start up Safety Review
Hot Work Permit
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response

## Slide 23: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Pre-Start up Safety Review
Hot Work Permit
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response

## Slide 24: The Elements of the PSM Standard
Application
Exclusions
Definitions
Employee Participation
Hazards of the Process
Toxicity
Technology of the Process
Equipment in the Process
Mechanical Integrity
Inspection & Testing
Quality Assurance
Process Hazard Analysis
Management of Change
Operating Procedures
Pre-Start up Safety Review
Hot Work Permit
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response

## Slide 25: The Elements of the PSM Standard
Let’s Explore Some of the Elements…

## Slide 26: Application
1910.119(a)

## Slide 27: What Facilities are Covered
Those Who Use Chemicals in Appendix A: A List of highly hazardous chemicals, toxics and reactive (Mandatory). Contains a listing of toxic and reactive highly hazardous chemicals which present a potential for a catastrophic event at or above the threshold quantity
Examples
  Chemical Threshold Quantity (TQ)
  Anhydrous Ammonia 10,000 lbs
  Chlorine 1,500 lbs

## Slide 28: What Facilities are Covered
A process which involves a flammable liquid or gas (as defined in 1910.1200(c) of this part) on-site in one location, in a quantity of 10,000 pounds (4535.9 kg) or more

## Slide 29: What Facilities are Covered
Important Interpretation: 2007 - 06/11/2007 - OSHA defines "on-site in one location" for Process Safety Management of Highly Hazardous Chemicals standard
OSHA interprets "on-site in one location" to mean that the standard applies when a threshold quantity of a highly hazardous chemical (HHC) exists within an area under the control of an employer or group of affiliated employers. It also applies to any group of vessels that are interconnected, or in separate vessels that are close enough in proximity that the HHC could be involved in a potential catastrophic release.

## Slide 30
Affect of the “Meer” Decision:
MEER ruling and the MEER Memorandum addressed in the Secretary's letter, OSHA's enforcement policy that the Agency would not cite employers for violations of 1910.119 where stored flammable liquids in atmospheric tanks were connected to a process, unless the process outside of the amount in storage contained more than 10,000 pounds of the substance
What Facilities are Covered

## Slide 31: What Types of Industries?
Industries that Process Chemicals Such As:
  Industrial Organics & Inorganics
  Paints
  Pharmaceuticals
  Adhesives
  Sealants and Fibers
  Petrochemical facilities
  Paper Mills
  Food Processing with Anhydrous Ammonia over the TQ

## Slide 32: Exclusions
1910.119(a)(1)(ii)(A)

## Slide 33: There are Exclusions
An employer is exempt from the requirements of PSM when:
A threshold quantity of flammable liquids is stored in atmospheric tanks or transferred without the benefit of chilling or refrigeration
Hydrocarbon fuels used solely for workplace consumption as a fuel (e.g., propane used for comfort heating, gasoline for vehicle refueling),
  If such fuels are not a part of a process containing another highly hazardous chemical covered by this standard

## Slide 34: There are Exclusions
Retail facilities;
Oil or gas well drilling or servicing operations; or,
Normally unoccupied remote facilities

## Slide 35: Employee Participation
1910.119(c)

## Slide 36: Now that we are required to comply, then what?
Form a Team in Your Company, i.e..
  Process Engineers
  Operators
  Safety
  Maintenance
  Management
  Consultants
Remember…You Can’t Do it Alone!

## Slide 37: Now that we are required to comply, then what?
Form a Plan, Determine:
  Responsibilities
  Duties
  Reporting
  Document Control
  Progress Reports
  Tracking Changes
Then…Begin the Process of Developing & Implementing the PSM Program

## Slide 38
Hazards of the Process
1910.119(d)(1)

## Slide 39
The Requirements of the Standard - Hazard Determination
Determine:
Chemicals in Your Process
Process Chemistry
Quantity of Chemicals in lbs
Compare to Appendix A List with Threshold Quantities (TQ’s)

## Slide 40
Toxicity Information
1910.119(d)(1)(i)

## Slide 41
The Requirements of the Standard - Develop Toxicity Information
Obtain Toxicity Information on the Chemical(s) in the Process
MSDS are Typical Resource
You May Need Other References, NIOSH Pocket Guide, ACGIH TLV’s

## Slide 42
Technology of the Process
1910.119(d)(2)

## Slide 43
The Requirements of the Standard - Process Technology
Block flow diagram or process flow diagram
Process chemistry
Maximum intended inventory
Upper and lower limits
Consequences of deviations

## Slide 44
The Requirements of the Standard - Process Equipment
Materials of construction
Process and instrument drawings (P&ID’s)
Electrical classification
Relief system design
Ventilation system design
Design codes
Material and energy balances
Safety systems

## Slide 45
Equipment in the Process
1910.119(d)(3)

## Slide 46
The Requirements of the Standard - Process Equipment
Now:
Identify Each Piece of Equipment in the Covered Process by P&ID, Block Diagram and Number Them
Remember - Must Follow Form
Must be Able to Track Each Number Through the Entire Program

## Slide 47
Mechanical Integrity
1910.119(j)

## Slide 48
Mechanical Integrity Certificates
Must be Obtained for Each Element of the Process
Must be Marked with Numbering System that Follows Form
The Requirements of the Standard - Process Equipment

## Slide 49
Process Hazard Analysis (PHA)
1910.119(e)

## Slide 50
Process Hazard Analysis (PHA’s)
Arguably the Most Difficult Part of Performing the Standard
PHA process is dynamic and subject to revision whenever changes are made
Performed by Your PSM Team
Takes Significant Time & Effort
PHA’s are Never Ending

## Slide 51
Process Hazard Analysis
A PHA Process Must be Performed on Each Element of the Covered Process:
A PHA From Block Diagram to P&ID to Every Equipment Component to Determine What Might Happen if an Element of the Covered Process Fails

## Slide 52: There is Much More to PSM
Inspection & Testing
Quality Assurance
Management of Change
Operating Procedures
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response
Incident Investigation
Compliance Audits
Trade Secrets
Notes: Inspection & Testing
Quality Assurance
Management of Change
Operating Procedures
Safe Work Practices
Training
Contractor Management
Emergency Planning & Response
Incident Investigation
Compliance Audits
Trade Secrets

## Slide 53: Management of Change
Procedures to manage changes to the covered process.
  Exception: “replacement in kind”
Management of Change includes:
  Process chemicals
  Technology
  Equipment
  Operating Procedures
  Facilities

## Slide 54: Management of Change Addresses
Technical basis of the change
Impact to employee safety and health
Modification to operating procedures
Time period for change
Authorization of change

## Slide 55: Operating Procedures
Develop and implement written operating procedures that are clear instructions for all expected phases of operations.
AKA – Standard Operating Procedures (SOPs)
Must cover:
  Operation phase
  Operational limits
  Safety & health considerations

## Slide 56: OPs Must Address
Initial start-up
Normal operations
Temporary operations
Emergency shutdown
Emergency operations
Normal shutdown
Start-up following turnaround
Consequences of deviation
Steps required to correct or avoid deviation

## Slide 57: SOPs
Must be readily available to employees
Must be reviewed as needed to ensure they reflect current operating practicce.
Must cover:
  Process chemicals
  Technology and equipment
  Facilities
SOPs must be certified annually that they are correct and accurate.

## Slide 58: Safe Work Practices (SWPs)
Must be developed and implemented to provide for the control of hazards during work activities such as:
  Lock-out/Tag-out
  Confined space entry
  Opening processes, piping or equipment
SWPs are for:
  Operators
  Maintenance personnel
  Contractors
  Lab personnel
  Or other support personnel

## Slide 59: Training
PSM specific training is required
Must cover:
  Safety and health hazards associated with the covered process
  Safe work practices
Refresher training is required every 3 years or as needed to ensure employees are complying with all PSM requirements

## Slide 60: Contractors
Contractors involved in or around a covered process must be informed of required PSM elements.
Contract work includes:
  Maintenance and repair
  Turn around
  Major renovations
  Specialty knowledge or services
  Does not include support services not involved with the covered process, like laundry or vending machine supply

## Slide 61: Emergency Action Plans (EAP)
Must have EAP for entire facility
EAP must have provisions for small releases of HHCs
Develop a Early Warning Method for Releases
Train on the Meaning of the Alarms
Develop Emergency Evacuation Written Plans, Evacuation Maps & Assembly Points

## Slide 62: Incident Investigations
Must be initiated ASAP, but within 48 hours
Team must include:
  Person knowledgeable in the process involved
  Includes contractor if work of the contractor involved
  Other persons with appropriate knowledge of the covered process

## Slide 63: Incident Investigation Report
Report must be produced with the following:
  Date of incident
  Date of start of investigation
  Description of incident
  Factors contributing to incident
  Recommendations
System must be established to promptly address recommendations and findings of report
Resolutions and corrective action must be documented

## Slide 64: Compliance Audit
To ensure that PSM is effective, employers must certify every 3 years that they have evaluated compliance with the standard
Must be completed by at least on person knowledgeable in the process
Report must be developed and documented
Deficiency corrections must be documented
Last two compliance audits must be kept on file

## Slide 65: Trade Secrets
Employers must make all necessary information required to comply with PSM, regardless of trade secrets, available to persons involved in developing or creating:
  Compiling process safety information
  PHAs
  SOPs
  Incident investigations
  Emergency planning and response
  Compliance audits
Confidentiality agreements are allowed

## Slide 66: BP Texas City Refinery Case Study in PSM
The third largest petroleum refinery in the United States with a refining capacity of 475,000 barrels of crude per day.
Located on a 1,200-acre facility in Texas City, Texas southeast of Houston in Galveston County.
1,200 permanent BP employees and hundreds of additional contractors at the facility

## Slide 67: Anatomy of a Disaster- BP Texas City
Things to Think About:
  What went wrong?
  What went right?
  What could/should have been done to prevent this disaster?

## Slide 68: BP Texas City Refinery Case Study in PSM

## Slide 69: JORDAN BARAB Deputy Assistant Secretary
After BP-Texas City, Have We Learned Anything?
Now, in spite of your efforts, we have to acknowledge that something is desperately wrong. The status quo isn't working.
In the past three months alone, 58 workers have died in explosions, fires and collapses at refineries, coal mines, an oil drilling rig, and a natural-gas-fired power plant construction site.
OSHA is particularly concerned about the recent number of serious incidents at refineries that have scalded, burned or struck down your fellow workers. We are tracking these catastrophes and looking for trends -- including problems resulting from aging facilities. Since the BP Texas City explosion in 2005, OSHA has counted over 20 serious incidents in refineries across the country.

## Slide 70: There is Much More to PSM
Now, The OSHA PSM National Emphasis Program for Refineries & Chemical Facilities & Severe Violator Enforcement Program (SVEP)

## Slide 71: OSHA National Emphasis Program (NEP) for Refineries & Chemical Facilities
Petroleum Refineries NEP
  Issued August 2009
Chemical Facilities NEP
  Issued July 2010

## Slide 72: Typical Standards Cited
1910.119 PSM – 249 violations
1910.147 Lock and Tag - 20
1910.120 Hazwoper - 19
1910.1200 Hazcom - 12
1910.146 Confined Space - 11
5A.001 General Duty - 9
1910.307 Hazardous Locations - 7

## Slide 73: Most Frequent NEP PSM Citations
(f)(1) Operating procedures…………..38
(d)(3) PSI pertaining to equipment ….28
(e)(3) PHA specific criteria……………26
(j)(4) MI Inspection & Testing ………..21
(e)(5) PHA recommendation ...………12
(l)(1) MOC implementation …………..12
1910.119

## Slide 74: Severe Violator Enforcement Program (SVEP)
This Instruction establishes enforcement policies and procedures for OSHA's Severe Violator Enforcement Program (SVEP), which concentrates resources on inspecting employers who have demonstrated indifference to their OSH Act obligations by willful, repeated, or failure-to-abate violations. This Instruction replaces OSHA's Enhanced Enforcement Program (EEP).

## Slide 75: Severe Violator Enforcement Program (SVEP)
References:
OSHA Instruction CPL 03-00-010, Petroleum Refinery Process Safety Management National Emphasis Program, August 18, 2009

## Slide 76: Severe Violator Enforcement Program (SVEP)
Enhanced Follow-up Inspections
Nationwide Inspections of Related Workplaces/Worksites
Increased Company Awareness of OSHA Enforcement
Enhanced Settlement Provisions
Federal Court Enforcement under Section 11(b) of the OSH Act
Bottom Line: OSHA is Serious About
Compliance and Enforcement of PSM

## Slide 77
EPA Risk Management Plans (RMP) Basics
CAA 112(r)

## Slide 78
One More Thing to Discuss… EPA Risk Management Plans (RMP)
Many Times Companies Who Must Comply with PSM, must also Comply with the Requirements of EPA Risk Management Plans (RMP)
The RMP Standard was to be a Mirror of the PSM Standard…Didn’t happen!
Remember…PSM Protects the Workforce, RMP Protects the Community

## Slide 79
EPA RMP
Basic Requirements
  Executive summary
  Registration
  Off-site consequence analysis
  Five-year accident history
  Emergency response plan
  Prevention program summary information
  Certification

## Slide 80
All Public Facilities in this Release Plume Must be Identified & Surveyed
Release Plume

## Slide 81: OSHA PSM Summary
PSM is a Comprehensive, Difficult Standard
Although it was Promulgated in 1991, Catastrophes Continue to Occur
Recognizing these Facts, OSHA has Developed a National Emphasis Program for Refineries and Chemical Manufacturers
More Emphasis Planned for all PSM Sites
There is Much More Work to be Done…
RMP Must Also be Considered for Many Facilities

## Slide 82: Tools for Additional PSM Assistance
PSM Checklist
  www.oshainfo.gatech.edu
OSHA Website
  www.osha.gov
Chemical Safety Board Website
  www.csb.gov