## Slide 1: Section 1- Lift Truck Fundamentals Section 2- Stability, Balance, And Capacity Section 3- Preoperational Inspection Section 4- Safety Guidelines for Operating Lift Trucks Section 5- Safe Load Handling Techniques Section 6- Refueling Gasoline, Diesel, And LP Lift Trucks Section 7- Battery Charging And Changing

## Slide 2: Why is Operator Safety Training Important ?
Reduce the risk of personal injury
Reduce the risk of product and property damage
It’s the law

## Slide 3: Accident Statistics
Chart: Accident Statistics
| Tipover | Struck by a lift truck | Struck by a Falling Object | Elevated Employee | Ran Off a Loading Dock | Improper Maintence
Column1 | 0.25 | 0.18 | 0.14 | 0.12 | 0.07 | 0.06
85 Fatalities 34,900 Serious Injuries

## Slide 4: Section 1 Lift Truck Fundamentals

## Slide 5: Powered Industrial Truck Standards 29 CFR 1910.178
Requirements
Formal Training Must Include:
Truck Related Topics Employer Certification: Name of operator
Work Related Topics Date of training
Practical Experience: Date of evaluation
Demonstrated by Trainer Identity of person(s) performing training and evaluation
Exercise by Trainee
Evaluation of Driving Skills:
On the Type of Truck You Operate
Recertify Every 3 Years
Refresher Training
Operates in Unsafe Manner
Near Miss
Changes in the Workplace
New Equipment
Involved in an Accident

## Slide 6: Truck Classification
Class 1 Class 5
Class 2 Class 6
Class 3 Class 7
Class 4

## Slide 7: Qualities of a Professional Lift Truck Operator
Is responsible
Arrives on time
Is rested, alert, and physically prepared
(If you are under prescribed medication that causes drowsiness, contact your supervisor)
Is knowledgeable about company rules
Wears required protective clothing and equipment
Uses safety equipment including the operator restraint system
Has a desire to learn
Is skilled and works to improve those skills
Keeps vehicle under control
Removes jewelry if required

## Slide 8: Operation and Maintenance Manual

## Slide 9: Legal Plates

## Slide 10: Danger, Warning, And Caution Labels

## Slide 11: Differences Between Lift Trucks And Automobiles
STEERING
WEIGHT
BRAKES
VISIBILITY
Forklifts steer differently than automobiles.
Forklifts brake differently than automobiles.
Visibility drive in the direction that gives you the best site
A forklift with a load may weigh 5 times more than an automobile.

## Slide 12: Lift Truck Terminology

## Slide 13: Lift Truck Fundamentals: Course Review
1) All lift trucks are required to carry a warning that improper operation or maintenance could cause injury or death.
True____ False____
2) What are the differences between lift trucks and automobiles?
A. Steering B. Vehicle weight C. Braking D. All the above
3) Federal OSHA regulations require all lift truck operators to be trained.
True____ False____
4) Driving evaluations must be done every year?
True____ False____
5) A lift truck could weight as much as 5 times more than and automobile?
True____ False____

## Slide 14: Section 2 Stability, Balance, And Capacity

## Slide 15: The Principle Of Balance
Fulcrum

## Slide 16: Center Of Gravity
The imaginary point in an object around which all weight is evenly distributed

## Slide 17: Load Center
Load center is defined as the distance from the face of the forks to the load’s center of gravity

## Slide 18: Static Conditions And Dynamic Forces
Static Conditions Dynamic Forces
Load Size
Load Weight
Height of the load
Amount of tilt
Tire Conditions
Traveling
Truck Speed
Applying the brakes
Surface conditions

## Slide 19: Capacity Plates

## Slide 20: Pivot Points
Keep the pivot point close to the INSIDE corner.
Where is the PIVOT POINT ?

## Slide 21: The Principle Of Stability
The stability triangle is formed by drawing a line between the 3 Point suspension of a lift truck.
Combined center of gravity
Longitudinal Stability
Lateral Stability

## Slide 22: Attachments And Effect On Capacity And Stability
Do attachments effect the trucks stability ?

## Slide 23: Stability, Balance, And Capacity: Course Review
1) The basic principle used by all lift trucks is the principle of balance and stability?
True____ False____
2) The center of gravity does not move?
True____ False____
3) Raising a load changes the truck’s center of gravity?
True____ False____
4) A load with an extra-long load center changes the balance of your truck?
True____ False____
5) Fork Extensions decrease the safe capacity of the lift truck?
True____ False____

## Slide 24: Section 3 Preoperational Inspection

## Slide 25: The Visual and Operational Inspection
Forks
Fork Locks
Cylinders
Chains
Hoses
Rollers
Channels
LOOK for Damage
Chunks
Separation
Flat spots
Low pressure
Horn
Unusual noise
Safety Belt
Warning devices
OSHA requires a daily inspection of the truck at the start of each shift by the operator.

## Slide 26: Internal Combustion / LP Trucks – Engine Compartment
Engine Oil
Hydraulic Oil
Trans. Fluid
Brake Fluid
Radiator if cool
Battery Levels
Follow Company Policies
Properly mounted tank
Pressure relief valve pointing up
Hose and connections
Tank restraint brackets
Leaks (Soapy water)
Check Tank for cracks dents
Check data stamp

## Slide 27: Electric Trucks

## Slide 28: The Operational Inspection
Report any defects immediately
Never operate a truck in need of repairs
Repairs shall be made by authorized and trained personnel

## Slide 29: Preoperational Inspection: Course Review
1) It is safe to change an LP tank inside a trailer at the loading dock?
True____ False____
2) Lift trucks should be inspected at the start of each shift?
True____ False____
3) Major leaks should be reported as soon as you spot one?
True____ False____
4) Forklift driver should check battery levels ?
True____ False____
5) You should operate a truck with a broken back-up alarm?
True____ False____

## Slide 30: Section 4 General Rules Of The Road

## Slide 31: Entering The Vehicle
3 point contact getting in or out of the vehcile

## Slide 32: Safety Guidelines When Operating A Lift Truck
EE
It’s the law
Stay out of restricted areas that your truck in not rated for
Keep three truck lengths between you and them

## Slide 33: Pedestrian Traffic
Using the horn properly , when and where

## Slide 34: Traveling On Ramps
Heavy end up hill if traveling on a grade more then 10 per cent

## Slide 35: Tractor Trailers And Railcars

## Slide 36: Parking Your Lift Truck
Attended Parking:
Driver is within 25 feet of the truck.
Unattended Parking:
Driver is more than 25 feet away. Truck is out-of- sight of the driver.

## Slide 37: General Rules Of The Road: Course Review
When passing a pedestrian you should sound your horn, make eye contact.
True_____ False_____
It is okay to stick your leg outside the operator’s compartment when carrying a wide load.
True_____ False_____
Railroad tracks should be crossed straight on.
True_____ False_____
When you are driving a truck on a ramps you can drive any direction you want.
True_____ False_____
If the load you are carrying obstructs your vision, just raise the load to get a better view.
True_____ False_____

## Slide 38: Section 5 Safe Load Handling Techniques

## Slide 39: Causes Of Tip - Over
How to handle freight properly

## Slide 40: Safe Load Handling
Assessing The Load
Fork Position
General Handling Techniques

## Slide 41: Safe Load Handling
Engaging A Load 2-8 inches load height
Inching Pedal
Executing Turns
Rear End Swing
Deploying Loads
Elevating Personnel

## Slide 42: Tip-Over Procedure
Always Fasten Seat Belt Anytime You Operate Your Truck
Never jump! Stay with the truck
Hold on tight
Brace your feet
Lean forward and away from the fall

## Slide 43: Safe Load Handling Techniques: Course Review
1) Always keep your foot on the brake pedal while selecting a direction?
True____ False____
2) Lift trucks pivot at the steering wheel?
True____ False____
3) Check with your supervisor when a load looks to heavy for your truck?
True____ False____
4) Use a spotter to help you travel with an oversized load?
True____ False____
5) Tilt the load full forward before you move the truck when stacking loads?
True____ False____

## Slide 44: Section 6 Refueling Gasoline, Diesel And LP Lift Trucks

## Slide 45: Basic LP Fuel Guidelines
Types Of Fuel Used In Internal Combustion Lift Trucks
PPE Personnel Protection Equipment
Company Policies
Carbon Monoxide

## Slide 46: LP Trucks

## Slide 47: LP / Gas / Diesel
General Safety Rules
Gasoline And Diesel Fueling
Liquid Petroleum (LP) Fuel
Characteristics of fuel
Basic Fuel Guidelines
Replacing LP/Gas

## Slide 48: Refueling Gasoline, Diesel, And LP Lift Trucks: Course Review
1. It is safe to change an LP tank inside a trailer at the loading dock.
True ____ False ____
2. Lift trucks should be inspected at the start of each shift.
True ____ False ____
3. Major leaks on your truck should be reported as soon as you spot one.
True ____ False ____
4. It’s not required to follow company policies.
True ____ False ____
5. You should operate a truck with a broken back up alarm.
True ____ False ____

## Slide 49: Section 7 Battery Charging And Changing

## Slide 50: Battery Charging And Changing
Battery Size Affects The Following:
Battery Hazards
Battery Safety
Changing Industrial Batteries
Charging an Industrial Battery in a truck
Watering Batteries
Ensuring Maximum Battery life

## Slide 51: Battery Charging And Changing

## Slide 52: Battery Charging and Changing: Course Review
1. Battery size affects:
a. Lifting capacity
b. Lift truck stability
c. Charge life
d. All of the above
2. If you are exposed to electrolyte, the first thing you need to do is:
a. Seek medical attention
b. Go to the nearest eyewash station and flush
c. Wait until the shift is over
d. None of the above
3. After charging the battery, always turn the charger off first before disconnecting the battery from the charger:
True___
False ___
4. Normally, you should add water to a battery only:
Before charging
It doesn’t matter when you add water
After charging
None of the above
Always follow your company polices:
True ___
False ___